METAL ROOF -   Installation Instructions for ST01 and ST02

Safety first! Metal roofs can be very slippery when wet or icy! Never work on a roof alone! Always tie yourself and ladder off! Always secure the Snow Terminator before installation. Be sure to wear gloves and safety glasses at all times. Before you even use a ladder, we recommend that you call the U.S. Department of Labor Occupational Safety & Health Administration 1-800-321-OSHA (6742) they have free information and guidelines for you to be SAFE when working on a roof.

Installation - when CDX or OSB sub-sheathing is the under metal roofing.                                                                                                                                                                                                                                                                     If you plan to cover a vent, or install above a protrusion the fastening to the roof is the same. On the roof set your Snow Terminator in the desired location. Mark the location where the metal roofing “rib” touches the Snow Terminator “flange”. Use a Reciprocating Saw or a small Angel Grinder with a metal cutting blade. Cut the Snow Terminator Flange so it will set flat on the metal roofing. See (Option 2) Touch-up the cut metal with metal paint. Clean and dry the metal surface. Position the tape sealant on bottom of flange, remove backing. Then Install the Snow Terminator with the screws provided. Do not over tighten to avoid stripping.    Note: No worries about cutting out parts of the flange, it is rated at 72,000 pounds of shear if all the holes were to be used. So you can cut up to 50% off and we will still guarantee the Snow Terminator for Life! Customer Service 541.285.1965

(Option 2) Installation – “Pole Barn” with NO sub-sheathing under metal After cutting flange - Set the Snow Terminator back to the desired location. Mark the center of the flange holes at the 4 corners or ends. Drive 16 penny nails through the 4 marks. From under the roof locate the 4 nails. Mark the location, drive the nails back out. Then install solid 2”x 4” blocking between the rafters or joists centered under the flange locations.                                                                                                 (Blocking is not needed if plywood sheathing is already installed.)

If you have any install questions, please contact us at

snowterminator@gmail.com